## Slide 1: Mapping

## Slide 2: What is a map?
It is a representation of something (Earth, stars, solar system, a building, etc…

## Slide 3: Uses of Maps
To determine where you are going.
To act as a model of Earth’s surface.
Used to locate various places
To show the distribution of various features or types of materials.

## Slide 4: Quick Review of Latitude and Longitude
Latitude
  Measured in degrees North and South of the Equator.
  Lines drawn parallel to each other running west to east.

## Slide 5: Quick Review of Latitude and Longitude
Longitude
  Measured in degrees East or West of the prime meridian.
  Lines drawn running North and South.

## Slide 6: Topography
The lay of the land.
Shows relief using contour lines.
  Relief- highs and lows of Earth’s surface.
  Relief can be calculated
    Take the difference between the highest point and the lowest.
    Ex: Mountain peak 20 m. lake 10m
      20m- 10m= 10m
      The relief of this area is 10m

## Slide 7: Reading a topographic map- Contour Lines
Lines on topographic maps.
Connect points of equal elevation.
  Everything connected to that line has the same elevation.
  Elevation- the distance something is above sea level. Sea level= 0m or 0ft.

## Slide 8: Reading a topographic map- Contour Intervals
Contour interval- gives the difference in elevation between 2 contour lines.
  Another indicator of height.
  Shown on maps as C.I.= 10ft.
  Used to count contour lines.
C.I.= 1000ft
How it will look on a map

## Slide 9: Reading a topographic map- Index Contours
A index contour is a contour line that is accentuated in thickness and is labeled with the appropriate measure of elevation.
Index contours occur every fifth contour line.
Help the map user read elevations on a map.
Red arrows indicate location of index contours.

## Slide 10: Reading a topographic map- Streams
The direction a streams is flowing is shown on a topographic map by the way a contour line crosses the stream.
Streams are shown as a blue line on maps.
When contour lines cross a stream it looks like an upside down V.
The point in the V points
upstream. It opens in the direction the water is flowing.

## Slide 11: Reading a topographic map- Depression Contours
Depression contours show areas of lower elevation.
Drawn like contour lines with marks on the inside.
Hachure marks- tick marks on inside of closed circle.

## Slide 12: Reading a topographic map- Hills
Hills are represented on a topographic map by a series of concentric contour lines in a rough circle

## Slide 13: Reading a topographic map- Slope
Closely spaced contour lines represent steep slopes.
Widely spaced contour lines represent gentle slopes.

## Slide 14: Reading a topographic map- Benchmarks
A benchmark is a place where exact elevation is known.
  Shown by a B.M. on map
  Ex: BM 60

## Slide 15: Reading a topographic map- Colors
The colors on a topographic map are symbolic of different map features.
  Blue = water
  Green = forest
  Brown = contour lines
  Black = cultural features (buildings, place names, boundary lines, roads, etc.)
  Red = principal roads
  Pink = urban areas
  Purple = revisions to an older map, compiled from aerial photos. If an area has become urbanized, this may be shown as purple shading on the new, revised map.

## Slide 16: Reading a topographic map- Map Scale
Map scale indicates your distance along the ground, or the amount of ground covered by the map.
USGS- United States Geologic Survey
  Ratio- 1:24000
  one unit on the map is equal to 24,000 units of the same size on the ground.
    Ex:1 inch on the map = 24000 inches on Earth.
      Or after converting 1 inch = 2000ft.
Bar scale-indicated by a line or bar with distances marked in miles, feet, or kilometers.

## Slide 17: Reading a topographic map- Map Scale

## Slide 18: Reading a topographic map- Profiles
A topographic profile is a cross-sectional view along a line drawn through a portion of a topographic map.
  It is like taking a slice out of a portion of the Earth and looking at it from the side.

## Slide 20
This powerpoint was kindly donated to www.worldofteaching.com
http://www.worldofteaching.com is home to over a thousand powerpoints submitted by teachers. This is a completely free site and requires no registration. Please visit and I hope it will help in your teaching.