## Slide 1: Electricity
April 23, 2007

## Slide 2: Applications of Electrostatics

## Slide 3: Electric Charge
Measured in COULOMBS
Six million trillion electrons is about - 1 C.
Six million trillion protons is about + 1 C.

## Slide 4: Electric Potential Energy

## Slide 5: Electric Potential Energy
This spring has more SPE when it is compressed

## Slide 6: Electric Potential Energy
This spring has more SPE when it is compressed
Likewise, these charges will have more potential energy when they are pushed closer

## Slide 7: Electric Potential Energy
PE equals the amount of work done to move a charge from one place to another.

## Slide 9: Electric Potential Energy
Which will have the larger electric potential energy?

## Slide 10: Electric Potential Energy
A – because it requires work to move it away from the negative charge.

## Slide 11: Electric Potential (volts)
EP = work/charge

## Slide 12: Electric Potential (volts)
Example: 1000 joules of work is done to move the charge q from far away to the place indicated. If q = 10 C, what is the electric potential at the new location?

## Slide 13: Electric Potential (volts)
Example: 1000 joules of work is done to move the charge q from far away to the place indicated. If q = 10 C, what is the electric potential at the new location?
Voltage = work/charge
V = 1000 J/10C = 100 Volts

## Slide 14: Electric Potential (volts)
What if the charge in the previous problem were now 100 C instead of 10? What would happen to the EP?

## Slide 15: Electric Potential (volts)
What if the charge in the previous problem were now 100 C instead of 10? What would happen to the EP?
IT WOULD BE THE SAME!!!
Work would also increase

## Slide 16: Electric Potential (volts)
Electric potential is associated with LOCATION, not CHARGE

## Slide 17: Electric Potential vs Potential Energy
Which charge has more electric potential?
Which has more potential energy?

## Slide 18: Is 5000 Volts Dangerous?

## Slide 19: Is 5000 Volts Dangerous?
NOPE!
When 1 million electrons are added to a neutral balloon, it has an electric potential of 5000 volts

## Slide 20: Potential Difference (voltage)
Difference in electric potential between two points.

## Slide 21: Potential Difference (voltage)
Difference in electric potential between two points.
Potential difference between A and B is 0
A
B

## Slide 22: Potential Difference (voltage)
Difference in electric potential between two points.
Now there is a potential difference
A
B

## Slide 23: Potential Difference
Batteries provide potential difference between one end of the circuit and the other

## Slide 24: Potential Difference
Batteries provide potential difference between one end of the circuit and the other
Charges flow from high to low electric potential

## Slide 25: Potential Difference (voltage)
Why aren’t birds on power lines shocked?

## Slide 26: Potential Difference (voltage)
Why aren’t birds on power lines shocked?
The Potential Difference between their feet is zero! (0 voltage)

## Slide 27: Current (I)
Net flow of electrons